Fenix E35UE Flashlight

Fenix E35UE 2016, out of question, can be treated as the very flexible mate indoor and outdoor. Measuring at only 4.8 inches in length, this handy flashlight delivers a surprisingly powerful 1000 lumens from only one 18650 Li-ion battery, and also compatible with two hardy CR123A batteries. Dual side switch works separately to realize operation simplicity of five general mode plus strobe and SOS, specially designed lock-out function avoids maloperation. Industrial design details such as digitally regulated output, IPX-8 waterproof structure present optimal user-friendliness.

Technical Parameters

| ANSI/PLATO FL1 | General Mode | Strobe | SOS |
| --- | --- | --- | --- |
|  | Turbo | High | Mid | Low | Eco |  |  |
| Output | 1000 Lumens | 450 Lumens | 150 Lumens | 50 Lumens | 8 Lumens | 1000 Lumens | 150 Lumens |
| Runtime | 1h 50min* | 4h | 11h 50min | 42h 30min | 150h | / | / |
| Distance | 160m (Max) |
| Intensity | 6400cd (Max) |
| Spot Beam Angle | 13° |
| Spill Beam Angle | 66° |
| Impact Resistance | 1m |
| Waterproof | IPX-8, underwater 2m |
| Accessories | Lanyard, spare O-ring |

Notice: The above-mentioned parameters (lab-tested by using Fenix ARB-L2-3400 18650 rechargeable Li-ion battery) are approximate and may vary between flashlights, batteries and environments.

*Due to the protective setup of automatically turning to High from Turbo after working 5 minutes, the runtime of the Turbo brightness level is the accumulated time.

- Utilizes Cree XM-L2 U2 LED with a lifespan of 50,000 hours

- Powered by one 18650 rechargeable Li-ion battery or two CR123A Lithium batteries

- 122mm length x 24mm diameter

- 72 grams (excluding battery)

- Dual side switch for fast and convenient operation

- Digitally regulated output maintains constant brightness

- Reverse polarity protection, to protect from improper battery installation

- Anti-roll and anti-slip body design

- Made of durable aircraft-grade aluminum

- Premium type Ⅲ hard-anodized anti-abrasive finish

- Toughened ultra-clear glass lens with anti-reflective coating

Operation Instruction

Master Switch: controls General mode and output selection.

Auxiliary Switch: controls Strobe and SOS mode.

ON/OFF

With the light off, press and hold the master switch for 0.5 seconds to enter into General mode, press and hold the auxiliary switch for 0.5 seconds to enter into Strobe mode.

With the light on, press and hold the master or the auxiliary switch for 0.5 seconds to turn off the light.

Mode Switching

With the light on,

Single-click the master switch to enter into General mode,

Single-click the auxiliary switch to enter into Strobe mode.

Output Selection

In General mode, single-click the master switch to cycle through Eco→Low→Mid→High→Turbo;

Strobe and SOS

Single-click the auxiliary switch to enter into Strobe mode,

Another click the auxiliary switch to cycle through Strobe→SOS.

Lock-out Function

Lock: Simultaneously press the two switches for 3 seconds (when the light is unlocked), the light will blink twice at Low and then go out, the light is locked.

Unlock: Simultaneously press the two switches for 3 seconds (when the light is locked), the light will be unlocked and power on the last-used output level.

Note: In locked status, the light only responds unlocking operation, press on any switch, the light will blink twice at Low to remind the light is under locked status.

Intelligent Memory Circuit

The flashlight memorizes the last brightness level used in the General mode, the next time it is turned on, it will recall that previously used brightness level.

Over-heat Protection

The flashlight will accumulate a lot of heat when it is working at Turbo and High brightness level. When it works at Turbo for 5 minutes, the flashlight will automatically downshift to High output to prevent the light from overheating. If the Turbo output is needed, please reset it again. But the flashlight could be damaged or the normal service life could be shortened because of continuous use like this.

Battery Specifications

| Type | Dimensions | Nominal Voltage | Usability |  |
| --- | --- | --- | --- | --- |
| Fenix ARB-L2 Series | 18650 | 3.6V/3.7V | Recommended | √ |
| Non-rechargeable Battery (Lithium) | CR123A | 3V | Usable | √ |
| Rechargeable Battery (Li-ion) | 18650 | 3.6V/3.7V | Cautious* | ！ |
| Rechargeable Battery (LiFePO4) | 16340 | 3.2V | Usable | √ |
| Rechargeable Battery (LiFePO4) | 18650 | 3.2V | Banned | × |

Warning: Please do not mix batteries of different brands, sizes, capacities or types. Doing so can cause damage to the flashlight or the batteries being used.

*18650 Li-ion batteries are powerful cells designed for commercial applications and must be treated with caution and handled with care.  Quality batteries with circuit protection will reduce the potential for combustion or explosion but cell damage or short circuiting are potential risks the user assumes.

Battery Replacement

Unscrew the light head to insert the battery with the anode side (+) toward the light's head, screw the light head back on.

Usage and Maintenance

- Disassembling the sealed head can cause damage to the light and will void the warranty.

- Fenix recommends using excellent quality battery. If the flashlight will not be used for an extended period, remove the battery, or the flashlight could be damaged by electrolyte leakage or battery explosion.

- Unscrew the tail cap one-half turn or take out the battery to prevent accidental activation during storage or transportation.

- Continuous working at Turbo brightness level, the light may activate over-heat protection or light beam trembling, to maintain normal status, please lower the brightness level to cool down the flashlight.

- Long-term use can result in O-ring wear. To maintain a proper water seal, replace the ring with an approved spare.

- Periodic cleaning of the battery contacts improves the flashlight's performance as dirty contacts may cause the flashlight to flicker, shine intermittently or even fail to illuminate for the following reasons:

Reason A: The batteries need replacing.

Solution: Replace batteries (Please confirm the correct installation of anode and cathode).

Reason B: The threads, PCB boards contact or other contacts are dirty.

Solution: Clean the contact points with a cotton swab soaked in rubbing alcohol.

If the above methods don't work, please refer to the warranty policy before contacting your authorized distributor.

Notice: The routine cleaning video can be watched and downloaded through Fenix official website, please log onto the service channel->“maintenance for light”.

# Product Warranty

Fenix will replace products with documented manufacturing defects within 15 days of purchase and repair a light free of charge within 5 years of purchase if problems develop with normal use; if repair is required after 5 years from the date of purchase, Fenix will charge for parts. The total repair fee is dictated by the cost of the replaced materials.

# Product Registration

Fenix suggests you register your product on the official website for Fenixlight Limited (www.fenixlight.com). You can get an extra six-month warranty period once you have successfully registered.

# Warning

The flashlight is a high-intensity lighting device capable of causing eye damage to the user or others. Avoid shining the light directly into anyone’s eyes.

FENIXLIGHT LIMITED

Tel: +86-755-29631163/83/93    Fax: +86-755-29631181

www.fenixlight.com

E-mail:info@fenixlight.com

Address: 8/F, 2nd Building, Dong Fang Ming

Industrial Center, 33rd District, Bao' an,

Shenzhen 518133, China